## Slide 1
-SATHVIKA BANDI (231EC150)
-ASRITH SINGAMPALLI (231EC110)
Verilog-Based CNN Accelerator on FPGA:CIFAR 10
Guided by: Sushil Kumar Pandey
1

## Slide 2
Introduction
  Deep learning models, especially CNNs, require significant computational power, making software-based implementations on CPUs and GPUs inefficient for real-time applications.
  To address this, our project develops a Verilog-based CNN accelerator for CIFAR-10 image classification, optimizing convolutional layers, neuron modules, and weight storage for high-speed and paralell processing
2

## Slide 3
Problem Statement
To develop a Verilog-based deep learning accelerator that enables real-time,high speed CIFAR-10 image classification by optimizing convolutional layers, neuron processing, and weight storage through hardware parallelism and pipelining.
3

## Slide 4
Objectives
Design and implement a reliable and efficient Verilog-based deep learning accelerator for CIFAR-10 image classification.
Ensure high-speed, inference with optimized convolutional, activation, and pooling layers.
Optimize memory usage and weight storage to support efficient computations.
Address factors such as real-time performance, low power and hardware limitations.
Explore potential enhancements and scalability for broader deep learning applications.
Convolution Neural Network (CNN) – Fundamental of Deep Learning
4

## Slide 5
Convolutional Neural Networks (CNNs): Verilog HDL Hardware Acceleration Principles: Designing circuits to perform specific computations faster or more efficiently than general-purpose processors. CIFAR-10 Dataset Simulation Paralellism and Pipelining Fixed-Point Arithmetic MAC Units Memory Modelling | 
Our Mission and Vision | 4
Our Goals | 5
Our Traction | 6
Our Market | 7
Key Concepts
5

## Slide 6
Methodology
  Research & Requirement Analysis: Study CNNs, Verilog design principles, CIFAR-10 task. Define accelerator architecture.
  Neural Network Architecture Design: Plan Verilog module hierarchy: neurons, layers, memory interfaces, activation logic, and convolution units.
  Pretrain weights
  Verilog Implementation: Write Verilog code for all modules (Convolution, FC, Pooling, etc.).
  Testing with Dataset: Use (pre-processed) CIFAR-10 data vectors in testbenches t
  Final Evaluation on FPGA & Documentation: Implementing on FPGA .Analyze simulation results.
6
Notes: The convolutional and fully connected layer weights were pretrained using Python on the CIFAR-10 dataset. The learned weights were extracted and converted into fixed-point (16-bit) format suitable for hardware implementation.

## Slide 7
Design and Implementation
1. Input Layer:
  Input Size: 1x32x32
    The CIFAR-10 images (originally 3×32×32) were converted to grayscale to simplify processing and hardware complexity.
2. First Convolution Layer:
  Output: 6x28x28
    Applies 6 filters of size 5×5 with stride 1 and no padding.
    Output size reduces from 32x32 → 28x28 because:
    Output size=32−5+1=28\text{Output size} = 32 - 5 + 1 = 28Output size=32−5+1=28
    Receptive Field: Each neuron in this layer looks at a 5×5 region of the input image.
Design and Implementation
7

## Slide 8
3. First Max-Pooling Layer:
Output: 6x14x14
Applies 2×2 max-pooling with stride 2.
Downsamples each feature map by a factor of 2:
28/2=14
4. Second Convolution Layer:
Output: 16x10x10
Applies 16 filters of size 5×5 over the 6 pooled feature maps.
Output reduces:
14−5+1=10
The number of channels increases to 16.
5. Second Max-Pooling Layer:
Output: 16x5x5
Again uses 2×2 max-pooling with stride 2.
Output size becomes:
10/2=5
8

## Slide 9
6. Flatten Layer:
Output: 1×400
The 16 feature maps of size 5x5 are flattened into a 1D vector of 400 values:
16×5×5=400
7. Fully Connected (Dense) Layers:
First Dense Layer:
Input: 1×400
Output: 1×84
Connects all 400 inputs to 84 neurons using standard matrix multiplication.
Second Dense Layer (Output Layer):
Input: 1×84
Output: 1×10
Maps to 10 classes of CIFAR-10.
Likely uses softmax activation for producing class probabilities.
Max Pooling Layer | NumPyNet
9

## Slide 10
8.Implementation and Bitstream Generation
Map your design onto the FPGA fabric.
  Generate the bitstream file (.bit) to program the FPGA.
9. On-Board Testing
Hardcoded the input image in the top module. The FPGA board displays the number of the classified image on the 7-segment display.
Verify real-time output.
Measured:
Inference latency=1.5ms
Accuracy match with software model
IEEE Standard 754 Floating Point Numbers | GeeksforGeeks
10

## Slide 11
Pipelining and Paralellism
1. Parallel Convolution Operations
Multiple filters are applied in parallel using dedicated MAC units.
2. Parallel Pixel Processing Within a Kernel
Pixels within a feature map region are processed concurrently.
3. Parallel Pooling
Pooling operations are performed in parallel.
1. Layer-Level Pipelining
Each layer operates independently with input/output buffers, enabling simultaneous execution across layers.
2. Stage Separation
Distinct functional stages minimize interference time.
11
Notes: The network is broken into pipeline stages, such as:
Stage 1: Input buffering and preprocessing
Stage 2: Convolution 1
Stage 3: Pooling 1
Stage 4: Convolution 2
Stage 5: Pooling 2
Stage 6: Flatten and Dense Layer 1
Stage 7: Dense Layer 2 and Output

## Slide 12
1
Outcomes
A complete, functionally verified Verilog codebase for a CNN accelerator targeting CIFAR-10.
Successful simulation demonstrating correct classification behavior for test vectors.
2
The verified Verilog design serves as a foundation for potential future FPGA synthesis.
3
Implemented on FPGA and checking for correctness and Analysis of simulated performance metrics
4
12

## Slide 13
Literature Review
Kumar & Madhumati (2023): Designed a CNN architecture for object detection on FPGA, emphasizing efficient integration of convolutional and pooling layers to balance performance and resource utilization.
Yan et al. (2023): Focused on the design and implementation challenges of mapping CNN architectures onto FPGA hardware, providing solutions for efficient deployment.
Nielsen (2019): Provided foundational concepts in neural networks and deep learning, offering essential insights into CNN structures and operations.
13

## Slide 14
References
Kumar, N. S., & Madhumati, G. L. (2023). Implementation of Convolutional Neural Networks on FPGA for Object Detection. *2023 14th International Conference on Computing Communication and Networking Technologies (ICCCNT)*. doi:10.1109/ICCCNT56998.2023.10307606. (Relevant for CNN architecture ideas)
Hailesellasie, M., Hasan, S. R., Khalid, F., Wad, F. A., & Shafique, M. (2018). FPGA-Based Convolutional Neural Network Architecture with Reduced Parameter Requirements. *2018 IEEE International Symposium on Circuits and Systems (ISCAS)*. doi:10.1109/ISCAS.2018.8351283. (Relevant for optimization ideas)
Yan, R., Yi, J., He, J., & Zhao, Y. (2023). FPGA-based Convolutional Neural Network Design and Implementation. *2023 3rd Asia-Pacific Conference on Communications Technology and Computer Science (ACCTCS)*. doi:10.1109/ACCTCS58815.2023.00058. (Relevant for design) Nielsen, M. (2019). *Neural Networks and Deep Learning*. Determination Press. (http://neuralnetworksanddeeplearning.com/) (Fundamental CNN concepts)
14